## Slide 1: Multiglycan

## Slide 2: Index
From Chuan-Yih
2015-08-14 2015-07-23 2015-05-02 2015-05-01 2015-04-03 2015-03-25
From TTU
2015-07-16 2015-04-03 2015-03-31

## Slide 3: From Chuan-Yih

## Slide 4: 2015-08-14

## Slide 5
Response to: 2015-07-16

## Slide 6: 2015-07-23

## Slide 7: Batch mode issue
I was able to finish 54 raw files on a 4 GB (3GB available) Windows 7 32 bits computer.
All graphs are generated
Can not replicate issues in your end
  Advice: change another pc or re-install OS to run

## Slide 8: Peak picking problem ~ Missing peak
1094.0742 - 1094.0653 =~ 8.14 PPM > 6 PPM (Peak picking threshold)
1093.5653 + 0.5 = 1094.0653 (expect 2nd mono)
1094.0715 - 1094.0688 =~ 2.46 PPM < 6 PPM (Peak picking threshold)
1093.5688 + 0.5 = 1094.0688 (expect 2nd mono)
 Can’t find Peak
 Found Peak

## Slide 9: Peak picking problem ~ Missing peak
6 PPM is suggested by Shiyue
  Some PPM between expected 2nd/3rd isotope peak and observed peak can greater than 10 PPM
The ways to solve this problem are
  Give a wider threshold
  Match mono only (no isotope pattern matching)
This also could result in quantitation inaccuracy.

## Slide 10: 2015-05-02

## Slide 14
Close mass due to adducts
+ =378.1890
+ NH3 =378.2002
Mass difference=0.0112, if permethylated glycan mass is ~3000 Da, then the difference is ~3.7ppm, which can not be resolved by our MS method.
For example
V.S.
[M+2H]2+
1119.5905
[M+H+NH4]2+
1119.5961

## Slide 15
Since this is from glycan: 4-5-1-0-0, this glycan has the retention time as 24.3

## Slide 16
1111.08 H*2 ;
1122.072 Na*1 ;H*1 ;
1133.063 Na*2 ;
1119.594 NH4*1 ;H*1 ;
1130.585 NH4*1 ;Na*1 ;
741.056 H*3 ;
748.3835 Na*1 ;H*2 ;
[M+2H]2+
[M+H+Na]2+

## Slide 17
Observed m/z | 4-4-0-1 |  | 4-5-1-0-0 | 
1119.589 | NH4*1,H*1 | 1119.594 (Δ=0.005 PPM 4.4) | H*2 | 1119.588 (Δ=0.001 PPM 0.89)
1130.57959 | NH4*1 ;Na*1 | 1130.5851 (Δ=0.00551 PPM 4.9) | Na*1 ;H*1 | 1130.579 (Δ=0.00059 PPM 0.52)
Indeed, these m/z can be matched to two different glycans, however 4-5-1-0 has smallest delta and more reasonable elution time. Currently my program report these two glycans and merge them into different glycan. So the peaks are counted twice. I will modify my program to solve this problem.

## Slide 18: 2015-05-01

## Slide 19: New updated
Only use relative abundance above this value

## Slide 20: Illustrate peak range

## Slide 21
 |  |  | PPM
1111.074 | 6-7-0-4-0 | NH4*2 ;H*2 ; | 5.400151204
1111.08 | 4-4-0-1-0 | H*2 ; | 0
1111.098 | 10-8-1-0-0 | K*2 ;Na*2 ; | 16.20045361
1122.066 | 6-7-0-4-0 | NH4*2 ;Na*2 ; | 5.347250444
1122.072 | 4-4-0-1-0 | Na*1 ;H*1 ; | 0
1122.109 | 8-9-1-1-0 | K*1 ;NH4*3 ; | 32.97471107
1133.013 | 9-9-0-4-0 | K*2 ;NH4*2 ;H*1 ; | 44.12817293
1133.063 | 4-4-0-1-0 | Na*2 ; | 0
1133.084 | 7-9-1-2-0 | NH4*1 ;H*3 ; | 18.53383263
1119.588 | 4-5-1-0-0 | H*2 ; | 5.359085526
1119.594 | 4-4-0-1-0 | NH4*1 ;H*1 ; | 0
1119.595 | 9-8-1-1-0 | K*1 ;H*3 ; | 0.893180921
1130.579 | 4-5-1-0-0 | Na*1 ;H*1 ; | 5.306987091
1130.585 | 4-4-0-1-0 | NH4*1 ;Na*1 ; | 0
1130.587 | 9-8-1-1-0 | K*1 ;Na*2 ;H*1 ; | 1.768995697
741.0153 | 7-7-0-1-0 | K*2 ;NH4*2 ;Na*1 ; | 54.92162536
741.056 | 4-4-0-1-0 | H*3 ; | 0
741.1596 | 5-7-1-2-0 | Na*4 ;H*1 ; | 139.8005009
748.3738 | 6-6-1-2-0 | NH4*1 ;Na*3 ;H*1 ; | 12.96126919
748.3835 | 4-4-0-1-0 | Na*1 ;H*2 ; | 0
748.3867 | 4-6-0-2-0 | H*4 ; | 4.275882619

## Slide 22
1111.08 H*2 ;
1122.072 Na*1 ;H*1 ;
1133.063 Na*2 ;
1119.594 NH4*1 ;H*1 ;
1130.585 NH4*1 ;Na*1 ;
741.056 H*3 ;
748.3835 Na*1 ;H*2 ;

## Slide 23: 2015-04-03

## Slide 25
1130.581, 4-4-0-1-0, NH4 * 1; Na * 1;

## Slide 26
1119.59, 4-4-0-1-0, NH4 * 1; H * 1;

## Slide 27: 2015-03-25

## Slide 29
Two new columns in Glycan files
  LinearRegression_Slope
  LinearRegression_intercept

## Slide 30
Choose concurrent file

## Slide 31: From TTU

## Slide 32: 2015-07-16

## Slide 33: Batch Mode Issue
The batch mode is not able to handle more than 15 raw files simultaneously. As you can see in the “MergeResult.csv”, we tried to process 18 raw files together, the last file shows “N/A” for all glycans. (Some times last two or three samples are all “N/A”. In other cases, Multiglycan crushed with >15 files loading.)
The “pic” folders do not contain all the peak construction information, when batch mode is used. (Most of time, only several of the “pic” folders are empty. The ones we uploaded is the worst case, only “Cell_Deter_SP_01” has 3 pictures.)

## Slide 34: Quantitation Issue
There are two issues with the newest version of Multiglycan.
1. Some peaks are not picked.
2. Some quantitation results agreed with Xcalibur while some quantitation results did not.
Examples are shown in the following slides.

## Slide 35
Issue Type 1
EICs of [28000+2H]2+
Clear Peak

## Slide 36
2.56
4.78
5.08
1
2.73
9.68
3.92
16.08
14.01
1
5.25
39.39
Issue Type 2: quantitation of same glycan in different files (Multiglycan and Xcarlibur gives different ratio)

## Slide 37
2.61
5.04
4.21
1
2.80
8.15

## Slide 38
Issue Type 2: quantitation of same glycan in different files (Multiglycan and Xcarlibur gives similar ratio)
2.48
3.82
3.06
1
1.68
4.66
2.96
4.62
3.57
1
2.08
6.44

## Slide 39: 2015-04-03

## Slide 41
Not real

## Slide 42
Wrong charge state

## Slide 43: 2015-03-31

## Slide 44
m/z=1114.0832
Wrong Peak since it’s not first mono
Similar issue exists in several other structures e.g. 3-5-0-0-0, 3-4-0-0-0
Dropbox\Chuan-Yih\Raw file and old results\R4_150319124400.raw

## Slide 45
Could not be found in Xcalibur using EIC

## Slide 46
Not real peak
Real

## Slide 47
High mannose is excluded in the exported xls file in the latest version of software, they were picked in the PIC file. I have uploaded the raw file and the processed results in dropbox